## Slide 1
Grigore Rosu
President and CEO at Runtime Verification, Inc.
Professor of Computer Science at the University of Illinois at Urbana-Champaign
RV-ECU: Certifiable
Runtime Verification
for Automobiles
https://runtimeverification.com

## Slide 2: Why Bother?
NSF (Phase I) and NASA (Phase II) SBIR grants
  Want to be sure technology is useful before developing it
What you can get from it
  Reduce or avoid car recalls
    Safety requirements not violated, dynamically updatable
      Even if car is hacked (no distinction between hacked or malfunctioning ECU)
  Easier compliance to ISO 26262 for safety
    Safety monitors generated automatically (provably correct)
  Enhanced communication between OEMs and suppliers
    Formal safety specifications will be required and shared
  Easier, better, faster testing
    Separation of major concerns: safety versus functionality

## Slide 3: Background
Modern automobiles highly computerized, including dozens of Electronic Control Units (ECUs) communicating over the CAN bus

## Slide 4: The Importance of Recall
Recall is the most important unsolved problem in automotive
Recalls are costly ($2B+) and bad for business, and software related recalls are (increasingly) common

## Slide 5: Software Complexity Trends
Source: "Automotive Embedded Software Verification and Validation Strategies", Shankar Akella, Emmeskay Advanced Technology Solutions
More ECUs, more money on electronics, more features, more code

## Slide 6: ISO 26262 Reshapes Safety
ISO 26262 changing the face of automotive: first functional safety standard, in response to growing software complexity trends
Both OEMs and suppliers scrambling for compliance

## Slide 7: Problem
Current state-of-the-art not ideal
  Formal safety requirements not available
    OEMs blame suppliers, suppliers blame OEMs
  ECUs developed by suppliers; code not available
  Poor CAN bus architecture
    Any ECU can send messages to any other ECU
    ECU sent messages cannot be stopped

## Slide 8: Proposal
RV-ECU: in charge of monitoring global safety
  Provably correct (both monitoring and recovery code)
ECUs locally monitored
  Their critical CAN bus messages “approved” by local monitors
  Local monitors communicate with RV-ECU
  Local monitors achieved by instrumentation or API
RV-
Global
monitor
Local
monitors

## Slide 9: Local vs. Global (RV-ECU) Monitor
All monitoring code (red) generated automatically from safety requirements; recovery code verified
  Certifiably correct (checkable proofs also generated)
Local monitors added through instrumentation (automatically) or provided API, and can
  Prevent ECU from sending wrong messages
  Consult with RV-ECU to assure global safety
  Add authentication
CAN Bus
ECU
ECU
RV-ECU
Global
monitor
Local
monitor
Usual ECU Code

## Slide 10: Example
Safe door lock
Doors should always open only if they were unlocked in the past and not locked since then; at violation, close door.
…(hundreds of these)
Informal requirements
Formalize requirements
(by domain experts,
using various formalisms;
here an interval logic)
 d : always (Open(d) implies
not Lock since UnLock)
@violation : Close(d)
Formal requirements
// One such monitor instance
// in RV-ECU for each door d
State: one bit, b
b = UnLock || !Lock && b
if (Open && !b)
then send(Close)
Monitor for each d
Automatically
generated
Provably correct

## Slide 11: Current RV-ECU Progress
Prototype RV-ECU on an STM ECU
board STM3210C-EVAL
  Working on a real car (model omitted)
    controlling wipers, windows, doors
    soon engine and brakes
For the time being, local monitors intended to be as simple as just requesting acknowledgements for messages to be sent on the bus from RV-ECU
  So RV-ECU does all monitoring, but local monitors ensure that safety violating messages are not sent

## Slide 12: Wrap Up
Certifiable runtime monitoring code generation
  Technology developed at the University of Illinois over a period of more than 12 years, funded with more than $6M by NSF, NASA, DARPA, NSA, Boeing
  Product for increasing safety in cars to be developed in our small company with SBIR funding from NSF, NASA, and research collaborations with automotive companies
    Main insight: separate safety from functionality and take no chances with safety (use highest assurance known for it!)
Practical impact sought:
  Looking for collaboration, partnership, leverage, matching funding (for our NASA and NSF grants)